## Slide 1: Adaptive Clocking Techniques for SoC Supply Droop Response in Predictive 7nm CMOS
Dan Fritchman, Wahid Rahman
EE241B Final Project
UC Berkeley
May 4, 2020

## Slide 2: Overview
Motivation
Adaptive clocking schemes
  PLL-based adaptive clocking
  Adaptive Clock Distribution (ACD)
PLL-based adaptive clocking in ASAP7
Simulation results
Summary

## Slide 3: Motivation
Power management in modern SoCs can enable/disable multiple cores, causing surge currents
Surge currents cause supply droops through L ripples from power distribution network
Objective: Adapt SoC clocking in response to supply droops with minimal guardbanding
Adapted from F. Ahmad et al. JSSC 2017
Adapted from T. Hashimoto et al. JSSC 2015

## Slide 4: Adaptive Clocking Schemes
Power supply sensor detects VDD change
Clock distribution (post-PLL) adjusts clock frequency by extending period
E.g. Phase rotators, tunable delay line
Power supply sensor detects VDD change
PLL internally adjusted for frequency
E.g. direct override of VCO, loop filter, divider
Actuation latency (i.e. adaptation time) is a key metric

## Slide 5: Actuation Latency Penalty
Longer TACT  lower VDD,ACT  lower fMAX
At fixed VDD:
Longer TACT  lower VDD,ACT  higher VMIN
At fixed fMAX:

## Slide 6: PLL-based adaptive clocking Hashimoto et al., JSSC 2015 (20nm CMOS)
ΔFCODE immediately adjusts DCO in response to sudden droop
  Sub-cycle logic latency + thermometer-coded logic (single AND gate)
NDIVSYNC filters droop through non-linear filter + moving average to track slower droops
  Helps re-lock PLL to nominal frequency after droop event
Low-latency logic claimed to improve fMAX by 7.5% (4.65GHz  5.00GHz) or 5% VMIN reduction at 4.65 GHz

## Slide 7: Adaptive clock distribution Wilcox et al., JSSC 2015 (28nm CMOS)
Phase rotator continuously extends period of CLKPLL to generate lower-frequency CLKSOC
40-phase DLL generates desired inputs to phase rotator mux
Longer actuation latency (3 clock cycles) than Hashimoto et al.
Up to 6% VMIN reduction reported at 4 GHz

## Slide 8: PLL-based adaptive clocking in ASAP7
KDCO = 60MHz/LSB (from PEX)
KP = 20, KI = 2-9
BW = 810kHz, PM = 79°
Logic latency = 40ps, DCO latency = 171ps (from PEX)
System-level simulation (MATLAB) with critical delays back-annotated from PEX

## Slide 9: C2MOS DCO Implementation
4-bit coarse DAC (initial lock)
4-bit fine DAC (PLL)
3-bit droop DAC

## Slide 10: RTL Implementation?

## Slide 11: Backend implementation

## Slide 12: Comparison to Prior Works

## Slide 13: Summary